## Slide 1: LASTT Training Package
Train your basic laparoscopic psychomotor skills
Version 2019-02

## Slide 2
Overview of Package Contents

## Slide 3: Box Contents
Wooden LASTT Model
Exercise inserts
Exercise elements
Stopwatch to record the time of the exercises
Leaflet and target sheets
Overview of Contents

## Slide 4
Online Scoring Platform

## Slide 5: Functionality
The LASTT Training Package is to be used together with the Online Scoring Platform (OSP), it allows you to:
  manage mentees participating in your sessions
  submit LASTT, SUTT and HYSTT training results
  see how your mentees relate to the benchmark group and see the group distribution
  validate when the minimal requirement for entry in the operating room is met
  issue branded reports for internal use
A license for the OSP can be acquired by going to www.id-trust-medical.eu
Online Scoring Platform

## Slide 6
Online Scoring Platform

## Slide 7
LASTT Exercises

## Slide 8: About LASTT
LASTT is a practical test to measure the competence level of an individual in basic laparoscopic psychomotor skills in the specific uterine environment:
  camera handling
  hand-eye coordination
  bi-manual coordination
LASTT Exercises

## Slide 9: Three Exercises
Exercise 1: Camera Navigation evaluates the skills to handle the camera and work with a 30° optic
Exercise 2: Hand-eye Coordination evaluates the skills of simultaneous camera and instrument handling
Exercise 3: Bi-manual Coordination evaluates the skills of bi-manual instrument handling
LASTT Exercises

## Slide 10: Conditions
Each exercise is performed 3 times
Exercises are done in pairs, where one mentee performs the exercise and the other assists
Pairs swap positions after each run
Mentee who assists is responsible for time registration and the scoring form
Scoring happens on the basis of time to correctly perform the exercise
LASTT Exercises

## Slide 11
Pelvic Trainer Port Position

## Slide 12: Szabo Pelvic Trainer
Port Position
6
5A
5B
4A
FORCEPS
4B
FORCEPS
3
CAMERA
2A
2B
1
Participant
CAMERA is introduced in the mid-central port (position 3) using a 10mm Trocar
FORCEPS in each of the central lateral ports (position 4A & 4B)
Correct orientation of the pelvic trainer: port 1-3 are closer together than 3-6

## Slide 13: Academy Pelvic Trainer
Port Position
FORCEPS
FORCEPS
CAMERA
Participant
CAMERA is introduced in the central port using a 10mm Trocar
FORCEPS in each of the lateral ports

## Slide 14
LASTT1 Exercise 1 Camera Navigation

## Slide 15: Aim
To navigate the camera and visualise the reach of all important areas of the pelvis
Camera handling with a 30° optic
Camera head in NON-DOMINANT Hand
Rotate light cable with your DOMINANT hand for correct view
Ex 1: Camera Navigation

## Slide 16: Setup
Equip the LASTT model with the character inserts
LASTT model is placed against the back wall of the pelvic trainer
Screen is equipped with a transparent target sheet which has a circle in the middle
Ex 1: Camera Navigation

## Slide 17: Starting Position
Place the optic so that both oblique panels and +heAcademy logo are in view (see picture) Maximum time of the exercise is 2 minutes
Ex 1: Camera Navigation

## Slide 18
Ex 1: Camera Navigation

## Slide 19: Procedure
Start your search by locating the first position 1a
Zoom in to position the target circle on the small character so that it is fully shown and readable
Only proceed when your partner can read the small character!
Ex 1: Camera Navigation
Search and locate the corresponding CAPITAL character (A)
Continue this sequence until you reach the last position with small character ‘end’

## Slide 20: Scoring
If the last position (end) is identified within 2 minutes, write down the time mm:ss:hh
If the last position (end) is not reached within 2 minutes, write down the last identified small character (e.g. 2f, Tn,…)
Ex 1: Camera Navigation

## Slide 21: Important
Ex 1: Camera Navigation
In order to minimise the memory effect, swap at least two inserts after each run

## Slide 22
LASTT1 Exercise 2 Hand-eye Coordination

## Slide 23: Aim
To evaluate the ability to navigate the camera with NON-DOMINANT hand
To handle a forceps with the DOMINANT hand
Ex 2: Hand-eye Coordination

## Slide 24: Setup
Remove the target sheet
Flip the two big inserts to show the colours on the oblique panels
Mount the 0° optic
Position 12 coloured rings by placing 2 of each colour in a circle around +heAcademy logo
Introduce the dissecting forceps using your DOMINANT hand
Ex 2: Hand-eye Coordination

## Slide 25: Starting Position
Ex 2: Hand-eye Coordination
In view:
The wooden model
Logo of +heAcademy with 12 coloured rings, 2 of each colour
Tip of the dissecting forceps

## Slide 26: Procedure
Ex 2: Hand-eye Coordination
Position ONE corresponding coloured ring on each nail
If you drop an object, you can use the second ring OR you may re-grasp, as long as you can find the object within the endoscopic boundaries
Maximum time of the exercise is 3 minutes

## Slide 27
Ex 2: Hand-eye Coordination

## Slide 28: Scoring
If all 6 rings are correctly placed within 3 minutes, write down the time mm:ss:hh
If time limit of 3 minutes is elapsed, write down the number of correctly placed rings
Ex 2: Hand-eye Coordination

## Slide 29
LASTT1 Exercise 3 Bi-manual Coordination

## Slide 30: Aim
To evaluate the ability to handle two forceps simultaneously with the DOMINANT hand and the NON-DOMINANT hand
Ex 3: Bi-manual Coordination

## Slide 31: Setup
Position 12 coloured pins around +heAcademy logo, 2 of each colour, plastic parts facing inwards.
Camera handling by the assistant with a 0° optic
Introduce the dissecting forceps using the DOMINANT hand and the grasping forceps in the NON-DOMINANT hand
Ex 3: Bi-manual Coordination

## Slide 32: Starting Position
In view:
The wooden model
Logo of +heAcademy with 12 coloured pins, 2 of each colour
Tips of both forceps
Ex 3: Bi-manual Coordination

## Slide 33: Procedure
Ex 3: Bi-manual Coordination
Position ONE coloured pin in each corresponding coloured target circle
Grasp plastic part of the pin with NON-DOMINANT hand and lift pin up
While elevated, pass the pin to the DOMINANT hand by grasping the metal part of the pin
Place the pin in the corresponding coloured circle and repeat for each colour
If you drop an object, you can use the second pin OR you may re-grasp, as long as you can find the object within the endoscopic boundaries

## Slide 34
Ex 3: Bi-manual Coordination

## Slide 35: Scoring
6 pins correctly placed within 3 minutes, write down the time mm:ss:hh
If time limit of 3 minutes is elapsed, write down the number of correctly placed pins
Ex 3: Bi-manual Coordination

## Slide 36
LASTT2 Exercise 1 Camera Navigation

## Slide 37: Aim
To navigate the camera and visualise the reach of all important areas of the pelvis
Camera handling with a 30° optic
Camera head in NON-DOMINANT Hand
Rotate light cable with your DOMINANT hand for correct view
Ex 1: Camera Navigation

## Slide 38: Setup
Equip the LASTT model with the character inserts
LASTT model is placed against the back wall of the pelvic trainer
Screen is equipped with a transparent target sheet which has a circle in the middle
Ex 1: Camera Navigation

## Slide 39: Starting Position
Place the optic so that both oblique panels and +heAcademy logo are in view (see picture) Maximum time of the exercise is 2 minutes
Ex 1: Camera Navigation

## Slide 40
Ex 1: Camera Navigation

## Slide 41: Procedure
Start your search by locating the first position 1a
Zoom in to position the target circle on the small character so that it is fully shown and readable
Only proceed when your partner can read the small character!
Ex 1: Camera Navigation
Search and locate the corresponding CAPITAL character (A)
Continue this sequence until you reach the last position with small character ‘end’

## Slide 42: Scoring
If the last position (end) is identified within 2 minutes, write down the time mm:ss:hh
If the last position (end) is not reached within 2 minutes, write down the last identified small character (e.g. 2f, Tn,…)
Ex 1: Camera Navigation

## Slide 43: Important
Ex 1: Camera Navigation
In order to minimise the memory effect, swap at least two inserts after each run

## Slide 44
LASTT2 Exercise 2 Hand-eye Coordination

## Slide 45: Aim
To evaluate the ability to navigate the camera with NON-DOMINANT hand
To handle a forceps with the DOMINANT hand
Ex 2: Hand-eye Coordination

## Slide 46: Setup
Remove the target sheet
Flip the two big inserts to show the colours on the oblique panels
Mount the 0° optic
Position 12 coloured rings by placing 2 of each colour in a circle around +heAcademy logo
Introduce the dissecting forceps using your DOMINANT hand
Ex 2: Hand-eye Coordination

## Slide 47: Starting Position
Ex 2: Hand-eye Coordination
In view:
The wooden model
Logo of +heAcademy with 12 coloured rings, 2 of each colour
Tip of the dissecting forceps

## Slide 48: Procedure
Ex 2: Hand-eye Coordination
Position ONE corresponding coloured ring on each nail
If you drop an object, you can use the second ring OR you may re-grasp, as long as you can find the object within the endoscopic boundaries
Maximum time of the exercise is 2 minutes

## Slide 49
Ex 2: Hand-eye Coordination

## Slide 50: Scoring
If all 6 rings are correctly placed within 2 minutes, write down the time mm:ss:hh
If time limit of 2 minutes is elapsed, write down the number of correctly placed rings
Ex 2: Hand-eye Coordination

## Slide 51
LASTT2 Exercise 3 Bi-manual Coordination

## Slide 52: Aim
To evaluate the ability to handle two forceps simultaneously with the DOMINANT hand and the NON-DOMINANT hand
Ex 3: Bi-manual Coordination

## Slide 53: Setup
Position 12 coloured pins around +heAcademy logo, 2 of each colour, plastic parts facing inwards.
Camera handling by the assistant with a 0° optic
Introduce the dissecting forceps using the DOMINANT hand and the grasping forceps in the NON-DOMINANT hand
Ex 3: Bi-manual Coordination

## Slide 54: Starting Position
In view:
The wooden model
Logo of +heAcademy with 12 coloured pins, 2 of each colour
Tips of both forceps
Ex 3: Bi-manual Coordination

## Slide 55: Procedure
Ex 3: Bi-manual Coordination
Position ONE coloured pin in each corresponding coloured target circle
Grasp plastic part of the pin with NON-DOMINANT hand and lift pin up
While elevated, pass the pin to the DOMINANT hand by grasping the metal part of the pin
Place the pin in the corresponding coloured circle and repeat for each colour
If you drop an object, you can use the second pin OR you may re-grasp, as long as you can find the object within the endoscopic boundaries

## Slide 56
Ex 3: Bi-manual Coordination

## Slide 57: Scoring
6 pins correctly placed within 2 minutes, write down the time mm:ss:hh
If time limit of 2 minutes is elapsed, write down the number of correctly placed pins
Ex 3: Bi-manual Coordination

## Slide 58
Questions?
info@europeanacademy.org