## Slide 1: SUTT Training Package
Train your laparoscopic stitching & knotting skills
Version 2018-07

## Slide 2
Overview of Package Contents

## Slide 3: Box contents
SUTT Foam Base
10 SUTT1 Pads for Training
10 SUTT2 Pads for Training
Pins to attach the SUTT Paper to the SUTT Foam Base
Stopwatch to record the time of the exercises
Overview of Contents

## Slide 4
Online Scoring Platform

## Slide 5: Functionality
The SUTT Training Package is to be used together with the Online Scoring Platform, it allows you to:
  manage mentees participating in your sessions
  submit LASTT, SUTT and HYSTT training results
  see how your mentees relate to the benchmark group and see the group distribution
  validate when the minimal requirement for entry in the operating room is met
  issue branded reports for internal use
A license for the OSP can be acquired by going to www.id-trust-medical.eu
Online Scoring Platform

## Slide 6
Online Scoring Platform

## Slide 7
SUTT Exercises

## Slide 8: About SUTT
Measure the ability of fine and complex motor skills by performing:
  correct stitches
  intra-corporeal knot
SUTT Exercises

## Slide 9: Conditions
Exercises are done in pairs, where one mentee performs the exercise and the other assists
All exercise runs are carried out and timed simultaneously under instruction of the head mentor
Scoring happens on the basis of time to correctly perform the exercise and quality: precision through the dots, correct pathway of the stitch, knot quality, absence of trauma
SUTT Exercises

## Slide 10
SUTT1 Exercise

## Slide 11: Aim
Measure the ability of fine and complex psychomotor skills by performing stitches using correct needle handling and intra-corporeal knot tying
SUTT1 Exercise

## Slide 12: Setup
Align the top of the SUTT1 paper with the second line from the top on the SUTT Foam Base
Securely attach the paper with 8 pins to the SUTT Foam Base
Place the SUTT Foam Base inside the Pelvic Trainer
SUTT1 Exercise

## Slide 13: Port Position
SUTT1 Exercise
6
5A
5B
4A
4B
1
CAMERA
3
Participant
2B
NEEDLE
HOLDER
2A
NEEDLE
HOLDER
CAMERA is introduced in the frontal middle port (position 1)
NEEDLE HOLDERS frontal lateral ports (position 2A & 2B)
TROCARS are optional
Correct orientation of the pelvic trainer: port 1-3 are closer together than 3-6

## Slide 14: Starting Position
In view:
Needle placed on the cross of the suturing pad, oriented at 3 o’clock
Tip of both needle holders
SUTT1 Exercise

## Slide 15: Procedure
Perform 4 single stitches using your dominant hand and 1 stitch with an intra-corporeal knot
Pass the suture by entering and exiting within the black dots
Leave enough thread in the pad for evaluation
Cut off using laparoscopic scissors
SUTT1 Exercise

## Slide 16: Procedure
Use ONE single 20 cm 2-0 poly-filament V-20 ½ 26 mm for the whole exercise
One of the five stitches, of your choice, must be secured and completed with an intra-corporeal surgical knot, i.e. double throw and two locking sequences
The exercise is timed until both ends of the thread are released at the end of the stitching or knotting movements.
SUTT1 Exercise

## Slide 17
SUTT1 Exercise

## Slide 18: Scoring
SUTT1 Exercise
Maximum time of the exercise = 15 minutes
Exercise finished within 15 minutes: write down the time mm:ss:hh
If not finished within 15 minutes: write down 15:00:00
QUALITY will be checked afterwards – leave threads on pad!

## Slide 19
SUTT2 Exercises

## Slide 20: Aim
Measure the ability of fine and complex motor skills by performing correct stitches and intra-corporeal knots.
SUTT2 Exercises

## Slide 21: Setup
SUTT2 Exercises
Align the top of the SUTT2 paper with the first line from the top on the SUTT Foam Base
Securely attach the paper with 8 pins to the SUTT Foam Base
Place the SUTT Foam Base inside the Pelvic Trainer

## Slide 22: Port Position
SUTT2 Exercises
6
5A
5B
4A
4B
1
CAMERA
3
Participant
2B
2A
CAMERA is introduced in the frontal middle port (position 1)
NEEDLE HOLDERS Your choice but position for each exercise must remain the same
TROCARS are mandatory
Correct orientation of the pelvic trainer: port 1-3 are closer together than 3-6

## Slide 23: 4 Exercises
SUTT2 Exercises
Exercise 1 Stitching Greek Suture
Exercise 2 Stitching & knot tying with right hand
Exercise 3 Stitching & knot tying with left hand
Exercise 4 Stitching, tissue approximation and knot tying with dominant hand

## Slide 24: Starting Position
In view:
Needle placed on the cross of the suturing pad, oriented at 3 o’clock
Introduce both needle holders
SUTT2 Exercises

## Slide 25: Ex 1: Greek Suture
SUTT2 Exercises

## Slide 26: Procedure
  15 cm 2-0 mono-filament V-20 ½ 26 mm.
  Start at red dot performing a left hand stitch
  Needle should be positioned correctly in dots
  Change hand after each stitch
  Be careful not to perform trauma
  Exercise timed until both ends of thread are released at end of the stitching movements.
Ex 1: Greek Suture

## Slide 27: Scoring
Maximum time of the exercise = 7 minutes
Exercise finished within 7 minutes: write down the time mm:ss:hh
Exercise not finished within 7 minutes: write down 7:00:00
QUALITY will be checked afterwards – leave threads on pad!
Ex 1: Greek Suture

## Slide 28: Ex 2: Right hand stitch & knot
SUTT2 Exercises

## Slide 29: Procedure
  Precise positioning of stitch on the predefined entry (red dot) & exit point (black dot)
  15 cm 2-0 mono-filament V-20 ½ 26 mm
  ONE intra-corporeal knot with flat knot and 2 locking sequences
  Exercise is timed until both ends of the thread are released at the end of the knotting movements
Ex 2: Right hand stitch & knot
SUTT 2

## Slide 30: Scoring
Maximum time of the exercise = 7 minutes
Exercise finished within 7 min: write down the time mm:ss:hh
Exercise not finished within 7 minutes: write down 7:00:00
QUALITY will be checked afterwards – leave threads on pad!
Ex 2: Right hand stitch & knot

## Slide 31: Ex 3: Left hand stitch & knot
SUTT2 Exercises

## Slide 32: Procedure
  Precise positioning of stitch on the predefined entry (red dot) and exit point (black dot)
  15 cm 2-0 poly-filament V-20 ½ 26 mm
  ONE intra-corporeal knot with flat knot and 2 locking sequences
  Exercise is timed until both ends of the thread are released at the end of the knotting movements
Ex 3: Left hand stitch & knot

## Slide 33: Scoring
Maximum time of the exercise = 7 minutes
Exercise finished within 7 minutes: write down the time mm:ss:hh
Exercise not finished within 7 minutes: write down 7:00:00
QUALITY will be checked afterwards – leave threads on pad!
Ex 3: Left hand stitch & knot

## Slide 34: Ex 4: Stitching, tissue approximation & knot
SUTT2 Exercises

## Slide 35: Procedure
  Precise positioning of stitch on the predefined entry & exit point with 15 cm 2-0 poly-filament V-20 ½ 26 mm
  Correct approximation of tissue by performing one intra-corporeal flat knot with 2 locking sequences
  Free choice of stitching hand
  Exercise is timed until both ends of the thread are released at the end of the knotting movements
Ex 4: Stitching, tissue approximation & knot

## Slide 36: Scoring
Maximum time of the exercise = 7 minutes
Exercise finished within 7 minutes: write down the time mm:ss:hh
Exercise not finished within 7 minutes: write down 7:00:00
QUALITY will be checked afterwards – leave threads on pad!
Ex 4: Stitching, tissue approximation & knot

## Slide 37
Questions?
info@europeanacademy.org